LEGO 2 LeJOS EV3
Library

Gripp3r Robot Version

# Introduction
The LEGO 2 LeJOS EV3 Library is intended to make it easy to port programs from the LEGO icon-based (LabView-based) programming system for the LEGO Mindstorms EV3 Brick to the Java programming language and the LeJOS EV3 framework.
This is the first version of the LEGO 2 LeJOS EV3 Library that supports the Gripp3r Robot.

# Gripp3r Robot
The Gripp3r Robot is a standard example available in the LEGO Mindstorms Programming Environment (Home Edition). You can download this Programming Environment at https://www.lego.com/en-us/mindstorms/downloads/download-software (or one of the other language pages). You also can find the building instructions of the Gripp3r Robot at https://www.lego.com/en-us/mindstorms/build-a-robot/gripp3r (or one of the other language pages).
Note1: The programs play sound sample files during movements of the gripper part of the robot. You can download them from:
http://tastyspleen.net/~quake2/baseq2/sound/world/airhiss1.wav and http://tastyspleen.net/~quake2/baseq2/sound/world/airhiss2.wav
Copy the sound files (via SCP) to the directory /home/lejos/lib on EV3 Brick before running the program.

Note2: The original Gripp3r mission 4 uses the touch sensor to close or open the gripper part of the robot. Instead of the Touch Sensor I use the top (beacon) button of the remote control to switch from the default move-around mode to the gripper movements: press the beacon button and then one of the upper buttons to open or close the gripper part.

# LEGO 2 LeJOS EV3 Library
The LEGO 2 LeJOS EV3 Library offers Java Developers various classes whose methods are similar to use as the LEGO icon-based Programming Blocks.
The LEGO 2 LeJOS EV3 Library depends on the LeJOS EV3 framework version v0.9.1beta.
You can find the LEGO 2 LeJOS EV3 Library at https://github.com/robl0377/Lego2LeJosEv3-Gripp3r. This project contains the following Java packages:
- lego2lejosev3.pblocks This is the package of the library classes.
- lego2lejosev3.logging This package contains some helper classes to use the standard java.util.logging package to write debug or error messages into a log file.
- lego2lejosev3.tests This package contains a few programs to test some features of the library.
- Lego2lejosev3.robots.gripper This package contains the main programs of the four ‘missions’ of the LEGO Mindstorms Home Edition Gripp3r project.

## How to use the Library
If you want to use the LEGO 2 LeJOS EV3 Library in your own LeJOS EV3 project, just copy the classes in the packages lego2lejosev3.pblocks and lego2lejosev3.logging into your project’s source location. The LeJOS Eclipse Plugin will pack them together with your own sources and download the whole JAR file to the EV3 brick to run it.

## Programming Blocks
LEGO provides descriptions of their icon-based programming Blocks in their web-based help pages for the LEGO Mindstorms Education Programming Environment.
There are the following Programming Blocks and their respective classes in the LEGO 2 LeJOS EV3 Library:
Action Blocks	LEGO 2 LeJOS EV3 Library
Medium Motor	MediumMotor Class
Large Motor	LargeMotor Class
Move Steering	MoveSteering Class
Move Tank	not yet implemented
Display	Display Class
Sound	Sound Class
Brick Status Light	not yet implemented
Flow Blocks
Start	use Java main method instead
Wait	use Java wait loop constructs instead, Utl Class
Loop	use Java loop constructs instead
Switch	use Java switch construct instead
Loop Interrupt	use Java break command instead
Sensor Blocks
Ultrasonic	not yet implemented
Infrared	InfraredSensor Class
Gyro	not yet implemented
Color	not yet implemented
Motor Rotation	not yet implemented
Touch	not yet implemented
Temperature	not implemented
Timer	not yet implemented
Brick Buttons	not yet implemented
Energy Meter	not implemented
NXT Sound	not implemented
Data Blocks
Variable	use Java global variables instead
Constant	use Java global static final variables instead
Array Operations	use Java array operations instead
Logic Operations	use Java logic operations instead
Math	use Java math operations instead
Round	use Java round operations instead
Compare	use Java compare operations instead
Range	use Java compare operations instead
Text	use Java String operations instead
Random	use Java Math.random method instead
Advanced Blocks
File Access	use Java file operations instead
Data Logging	use Java file operations instead
Messaging	not yet implemented
Bluetooth Connection	not yet implemented
Comment	use Java comments instead
Keep Awake	not yet implemented
Raw Sensor Value	not implemented
Stop	use System.exit method instead
Invert Motor	not yet implemented
Unregulated Motor	not yet implemented

Note: Since numeric operations in Java on the EV3 Brick are faster with float numbers than double numbers, please use float or int numbers whenever possible.

### Logging Mechanism
The LEGO 2 LeJOS EV3 Library uses the classes of the package java.util.logging, that come with the Java Runtime System, to write log, warning or error messages to log files. You can use this logging mechanism for debugging, warning or error messages in your own classes as well.
To use the logging mechanism it should be initialized as early in the program execution as possible. Here is an example:
import java.util.logging.Logger;
import lego2lejosev3.logging.Setup;

public class Gripp3rM1 {
private static Class<?> clazz = Gripp3rM1.class;
private static final Logger log = Logger.getLogger(clazz.getName());

public static void main(String[] args) {
Setup.log2File(clazz);
log.fine("Starting ...");
...
log.fine("The End");
}
}

In this example the main class of the program instantiates a logger with the class’ name and initializes logging to files with the method Setup.log2File(clazz). This initialization only needs to be done once in a program at the beginning of the main() method.
Then you can use the logger’s methods, such as fine() to write messages to the log file.
Other classes just need to instantiate a logger with their class name to use its methods.
The initialization sets a simple custom log formatter and configures the log files for 3 generations with a maximum of 2MBytes size each. Each run of the program starts a new log file in the same directory where the program’s JAR file is located (/home/lejos/programs/). You can download the log files with SCP or with the LeJOS EV3 Control Center.
For more information about the java.util.logging package, see Java™ Logging Overview.

### MediumMotor Class
The Medium Motor Block controls the Medium Motor. You can turn the motor on or off, control its power level, or turn the motor on for a specified amount of time or rotations.
The MediumMotor class that implements this block needs to be instantiated before its methods can be used, for example at the beginning of the program:
public class Gripp3rM1 {
static final Port gripMotorPort = MotorPort.A;

public static void main(String[] args) {
MediumMotor mot = new MediumMotor(gripMotorPort);
...
}
}

Several of the following programming blocks have power or brake at end inputs:
You can control the speed and direction of the motor using the power input. The power input accepts a number from -100 to 100. A positive number turns the motor clockwise, and a negative number turns it counter-clockwise.
If brake at end is true, the motor is stopped immediately. The motor will be held in its stopped position until another Motor block starts that motor, or until the program ends. If brake at end is false, power to the motor is simply turned off. The motor will coast using any remaining momentum until it stops, or until another Motor block starts.

Mode On:
The On mode turns the motor on, then immediately continues to the next block in the program. The motor will run until it is stopped or changed by another block later in the program, or until the program ends.
Signature:
public void motorOn(int power)
Example:
mot.motorOn(-75);

Mode Off:
The Off mode turns the motor off. It is usually used to stop a motor that was started by the On mode.
Signature:
public void motorOff(boolean brake)
Example:
mot.motorOff(true);

Mode On For Seconds:
On for Seconds turns the motor on for the number of seconds in the period input, then turns it off. The block will wait until the time has passed before the program will continue to the next block. Use true for brake at end to stop the motor after exactly the specified number of seconds.
Signature:
public void motorOnForSeconds(int power, float period, boolean brake)
Example:
mot.motorOnForSeconds(100, 0.9F, true);

Mode On For Degrees:
On for Degrees turns the motor on for the number of degrees specified in the degrees input, then turns it off. 360 degrees results in one full turn or rotation of the motor. Use true for brake at end to stop the motor after exactly the specified number of degrees.
Signature:
public void motorOnForDegrees(int power, int degrees, boolean brake)
Example:
mot.motorOnForDegrees(100, 850, true);

Mode On For Rotations:
On for Rotations turns the motor on for the number of rotations in the rotations input, then turns it off. Use true for brake at end to stop the motor after exactly the specified number of rotations.
Signature:
public void motorOnForRotations(int power, int rotations, boolean brake)
Example:
mot.motorOnForRotations(75, 3, true);

### LargeMotor Class
The Large Motor block controls a Large Motor. You can turn a motor on or off, control its power level, or turn the motor on for a specified amount of time or rotation.
The LargeMotor class that implements this block has the same methods as the MediumMotor Class.

### MoveSteering Class
The Move Steering block can make your robot drive forward, backward, turn, or stop. You can adjust the steering to make your robot go straight, drive in arcs, or make tight turns.
Use the Move Steering block for robot vehicles that have two Large Motors, with one motor driving the left side of the vehicle and the other the right side. The Move Steering block will control both motors at the same time, to drive your vehicle in the direction that you choose.
The MoveSteering class that implements this block needs to be instantiated before its methods can be used, for example at the beginning of the program:
public class Gripp3rM2 {
static final Port leftMotorPort = MotorPort.B;
static final Port rightMotorPort = MotorPort.C;

public static void main(String[] args) {
MoveSteering mst = new MoveSteering(leftMotorPort, rightMotorPort);
...
}
}

Several of the following programming blocks have power, steering or brake at end inputs:
You can control the speed and direction of the motors using the power and steering inputs. The power input accepts a number from -100 to 100. Positive and negative numbers for power make the motor turn in different directions.
The steering input accepts a number from -100 to 100. A value of 0 (zero) will make your robot drive straight. A positive number (greater than zero) will make your robot turn to the right, and a negative number will make your robot turn to the left. The farther the steering value is from zero, the tighter the turn will be.
If brake at end is true, the motors are stopped immediately. The motors will be held in their stopped position until another Move or Motor block starts them, or until the program ends. If brake at end is false, power to the motors is simply turned off. The motors will coast using any remaining momentum until they stop, or until another Move or Motor block starts.

Mode On:
The On mode turns both motors on, then immediately continues to the next block in the program.
The motors will run until they are stopped or changed by another block later in the program, or until the program ends.
Signature:
public void motorsOn(int steering, int power)
Example:
mst.motorsOn(0, 75);

Mode Off:
The Off mode turns both motors off. Use the Off mode to stop a robot that was started by the On mode earlier in the program. See the example above.
Signature:
public void motorsOff(boolean brake)
Example:
mst.motorsOff(true);

Mode On For Seconds:
On for Seconds turns both motors on for the number of seconds in the period input, then turns them off. The block will wait until the time has passed before the program will continue to the next block. Use Brake at End to stop your robot after exactly the specified number of seconds.
Signature:
public void motorsOnForSeconds(int steering, int power, float period, boolean brake)
Example:
mst.motorsOnForSeconds(0, -75, 2.0F, true);

### Mode On For Degrees:
On for Degrees turns both motors on, waits until one of them has turned for the number of degrees of rotation in the degrees input, and then turns both motors off. This can be used to make your robot travel a specific distance or turn a specific amount. 360 degrees of rotation corresponds to one full turn of a motor. Use brake at end to stop your robot after exactly the specified number of degrees.
Signature:
public void motorsOnForDegrees(int steering, int power, int degrees, boolean brake)
Example:
mst.motorsOnForDegrees(100, 75, 850, true);

Mode On For Rotations:
On for Rotations turns both motors on, waits until one of them has turned for the number of rotations in the rotations input, then turns both motors off. This can be used to make your robot travel a specific distance or turn a specific amount. Use brake at end to stop your robot after exactly the specified number of motor rotations.
Signature:
public void motorsOnForRotations(int steering, int power, int rotations, boolean brake)
Example:
mst.motorsOnForRotations(0, 75, 3, true);

### Display Class
The Display block can display text or graphics on the EV3 Brick display.
Many of the Display block modes use x and y coordinates to specify where to draw an item. The coordinates specify a pixel position on the EV3 Brick display. The position (0, 0) is at the upper left corner of the display.
The display is 178 pixels wide and 128 pixels high. X coordinate values range from 0 at the left of the display to 177 at the right. Y coordinate values range from 0 at the top to 127 at the bottom.

Mode Image:
The Image mode draws a graphic image file.
The filename input lets you choose the image file. This makes it easy to use the same image multiple times in a program or project. The image file must already reside on the EV3 brick. Please upload it (by SCP) to the /home/lejos/lib/ directory before using this programming block.
If clearScreen is true, the display will be cleared before the image is drawn.
The x and y inputs specify the Display Coordinates for the upper left corner of the image. The image will be drawn below and to the right of this point, using as much space as necessary to draw the entire image. For image files that are sized to fill the entire display, use x = 0 and y = 0.
Signature:
public static void image(String filename, boolean clearScreen, int x, int y)
Example:
n/a

Mode Reset Screen:
The Reset Screen mode clears the EV3 Brick display.
Signature:
public static void resetScreen()
Example:
n/a

### Sound Class
The Sound block makes sound using the speaker inside the EV3 Brick. You can play pre-recorded sound files or specify a musical note or tone.
Several of the following programming blocks have volume or playType inputs:
The volume input controls how loud the sound will be. Set it from 0 to 100 percent of full volume.
The playType input controls whether the block will wait for the sound to finish before the program continues to the next block, and whether the sound will repeat:
Sound.WAIT = 0: Wait for Completion: The sound plays once, and the program waits for the sound to finish before continuing.
Sound.ONCE = 1: Play Once: The sound plays once, and the program continues immediately.
Sound.REPEAT = 2: Repeat: The sound will be repeated continuously until another Sound Block is executed, and the program continues immediately.

Mode Play File:
The Play File mode plays a pre-recorded sound file.
The filename input lets you choose the sound file to play. This makes it easy to use the same sound multiple times in a program or project. The sound file must already reside on the EV3 brick. Please upload it (by SCP) to the /home/lejos/lib/ directory before using this programming block.
Signature:
public static void playFile(String filename, int volume, int playType)
Example:
Sound.playFile("airhiss1.wav", 100, Sound.ONCE);

### Utl Class
The Utl class implements one mode of the LEGO Wait Programming block only. The other modes can easily ported to simple Java wait loop constructs.

Mode Time:
In the Time mode, the Wait block waits for the amount of time you specify in the period input. The time is measured from the start of the Wait block.
Signature:
public static void waitTime(float period)
Example:
Utl.waitTime(1F);

### InfraredSensor Class
The Infrared Sensor block gets data from the Infrared Sensor. You can measure sensor data in the Proximity, Beacon, and Remote modes and get Numeric output.
The InfraredSensor class that implements this block needs to be instantiated before its methods can be used, for example at the beginning of the program:
public class Gripp3rM3 {
static final Port irSensorPort = SensorPort.S4;

public static void main(String[] args) {
InfraredSensor irs = new InfraredSensor(irSensorPort);

...
}
}

Mode Measure Proximity:
The Measure – Proximity mode uses the Infrared Sensor in Proximity mode. The proximity value (0 to 100) is an indicator for an object’s distance. Zero (0) means very close, and 100 means far away. The Proximity will be 100 if the object is not detected at all.
Signature:
public void setProximityMode()
public float measure()
Example:
irs.setProximityMode();
float value = irs.measure();
Note: This block is implemented by two separate method calls. I might collapse them into a single method in future versions of the library.

Mode Compare Proximity:
The Compare Proximity mode compares the sensor data to the threshold value using the selected operator (Compare Type). The true/false result is output in compare result.
The Compare Type supports the following values:
CompareType.EQUAL	= 0: = (Equal to)
CompareType.NOT_EQUAL	= 1: ≠ (Not Equal to)
CompareType.GREATER	= 2: > (Greater than)
CompareType.GREATER_EQUAL	= 3: ≥ (Greater than or Equal to)
CompareType.LESS	= 4: < (Less than)
CompareType.LESS_EQUAL	= 5: ≤ (Less than or Equal to)
Signature:
public void setProximityMode()
public boolean waitCompare(int operator, float threshold)
Example:
irs.setProximityMode();
irs.waitCompare(CompareType.LESS, 25F);
Note: This block seems a lot of effort to hide a simple comparison and wait loop that you can write easily in the Java programming language. I might not include it in future versions of the library.